MASON COUNTY ROAD COMMISSION

510 E. STATE ST.       PO BOX 247

SCOTTVILLE, MI.  49454

Will be accepting bids until : 10 AM  Tuesday January 12, 2016

for the following:

Two (2)  New Tandem Drive Semi Tractors

Four pages total include the specifications and bid form

Please note if  you comply or any deviations  for each item.

Make  _______________________   Model________________________

GVW     62,0000 lbs     ______________________

FRONT AXLE:   16,000 lb.  With dual steering gearboxes   ___________

ENGINE:      Cummins-ISX  --  550 hp  @1700 RPM  _________________

TRANSMISSION :  Fuller RTLO 18918B  18 speed  __________________

CLUTCH:   15 ½  manual adjustment  state model  ____________________

REAR SUSPENSION:  Air ride  state type  ___________________________

FRAME:     Full length heavy duty single   state spec  _____________________

WHEELBASE  181in.    _________________________________________

FRONT AXLE :  16,000 lb. w/ Tapered leaf front springs  _______________

REAR AXLE :   Spicer D46-170 HP with pump/filter ___________________

pg 1

REAR AXLE RATIO:   3:91    _____________________________________

DRIVER CONTROLLED  WHEEL LOCK both axles   ___________________

BRAKES FRONT & REAR :  16.5 in.    S-Cam  style  __________________

AIR SYSTEM:    18.7 CFM min.  w/ Bendix  AD-IS  air drier  ___________

16 ft.  trailer air lines    ___________________________

FIFTH WHEEL :  Holland Airslide  FW35-8001T3L   __________________

FRONT TIRE / WHEELS :   22.5in center hub aluminum wheels

and Goodyear G296 tires   __________________________________

REAR TIRE/WHEELS:  22.5in center hub aluminum wheels

and GoodyearG182RSD 14 ply tires   __________________________

WET KIT :   60 gallon hydraulic tank  right side  ____________________

PTO air control  in cab  __________________________________

Left side Transmission Provision for Customer mounted PTO _____

Clearance of Air tanks etc for PTO left mount      _________________

ELECTRICAL :

Batteries:  Three  AGM type In cab under passenger seat ___________

Master  Electrical Disconnect Switch  _________________________

Alternator:  130 amp min.  ____________________________________

Auto circuit breakers in place of fuses   __________________________

16 foot trailer light cable   _________________________________

Additional 7-way receptacle BOC prewired to accessory switches in

the dash . Combination of battery and ignition powered.___________

Pg 2

CAB: Extended day  cab for more back & head room.__________

Quiet Cab Package    ____________________________

Sloped  Hood   __________________________________

Telescoping Steering Column    _____________________

Full Mechanical Gauge Pkg. _________________________

AM/FM Radio   ___________________________________

Air Conditioning   ________________________________

Electric Horn   _________________________________________

Dual roof mounted air horns  ______________________________________

Air Ride Cab  ______________________________________________

Electric Windows and Door Locks   _______________________________

Full Rubber /Vinyl floor mats  ____________________________________

Seat: Cloth air ride with armrests    _________________________________

West Coast style mirrors with right side motorized    __________________

Exterior Sun visor   ______________________________________________

Trans and Axle temp gauge    _____________________________________

Engine Block Heater    __________________________________

Front Tow Hooks    ______________________________________

Fuel Tank  150 gallon  LH  aluminum   __________________________

Front wheel fender extensions   _______________________________

PAINT :     Cab   White   (Any other colors will be considered)

FRAME:    Black

Dealer to establish road speed and other perimeters with Mason CRC

shop before delivery.

Vehicle to meet all Federal, State and local safety standards.

Price to be FOB  Mason County Road Commission garage,

510 E. State St.  Scottville, MI.  49454

Tax exempt certificate will be provided upon request.

Any questions can be directed to Terry Woirol-   231-690-2554

Pg 3

BID FORM

Sealed bids will be opened and read on

TUESDAY  JANUARY 12 , 2016   at 10 AM

TOTAL BID PRICE  ACCORDING TO ABOVE SPECIFICATION.

$ ____________________ EACH

$ ____________________  TOTAL FOR (2) TWO TRUCKS

CAN A END OF APRIL 2016  DELIVERY BE MET?  _____________

BUYBACK OPTION  AFTER 1 YEAR    _

specify terms on separate sheet  ________________________

The undersigned hereby certifies  that he/she has examined, and has the

authority to submit, this bid proposal and is fully informed as to the nature

of the equipment to be furnished. All  the above conditions will be equal

or exceeded, and all requested information has been completed.

COMPANY NAME  ________________________________

ADDRESS       ___________________________________

_______________________________________

SUBMITTED BY       _________________________________

TELEPHONE #     _____________________________________